## Slide 1
Lecture 4
Computer Architecture

## Slide 2: Computer System Components
A computer set has the following major elements:-
Input devices
Output devices
The processors (CPU)
The storage devices

## Slide 3: Computer Architecture
The organization of computer Hardware is based on the Von-Newman Architecture, which is based on the concept of binary representation of numbers in the computer. This organization, also known as the computer theoretical organization, describes how the different types of computer hardware interact with each other, in the processing of data, so that the desired results can be achieved.

## Slide 4: The figure below illustrates the architecture:

## Slide 5: Hardware Devices
System Unit
Printer
Output Device
Peripheral
Monitor
Output Device
Peripheral
Input Device
Storage
Device
Input Device

## Slide 6: Peripheral devices
These are equipment that are used with the computer but are not integral part of it. They include printers, keyboards, monitors, mice, disk drives.
Input Devices
Input refers to the process of entering programs, commands, user responses and data into main memory. The most common input devices are:
Keyboard:
Users input data to a computer by pressing the keys on the keyboard. As the user enters the data on the Keyboard it displays on the screen.

## Slide 7: Keys on A Keyboard:-
The function keys labeled with letters F1 - F12. Which perform different tasks depending on the software program you are using.
The arrow keys/cursor control keys used to move the cursor.
The Data Keys used to enter the letters, numbers and symbols.
Special purpose keys e.g. Backspace, Del. Shift, Alt., Ctrl, Enter ,Esc., Pause etc.

## Slide 8: The most common input devices Cont’
Mouse
This is a small lightweight device that easily fits in the palm of your hand. Software programs designed to use mouse display a mouse pointer on the screen. The pointer may be an arrow, small rectangle, an I-beam or even a hand with a pointed finger.
To move the pointer, you gently slide the mouse around the mouse pad. Mouse has a language of its own.
Trackball
It is a pointing device that is used as an alternative to a mouse. You roll the ball to position the pointer on the screen. Unlike the mouse, a trackball doesn’t move on the desk and therefore requires less space.
Scanners
Scanners convert texts, characters or images into a form that can be processed by the computer

## Slide 9: Other input devices include
Touch screens
Graphic input
Optical character reader (OCR)
Optical mark reader (OMR)
Magnetic ink character recognition (MICR)
Microphones – For inputting sound/ Voice
Cameras – For capturing pictures and images

## Slide 10: The System Unit
The system unit also known as a base unit, is the main body of a desktop computer of the computer system.
The front part has the following buttons:-
  Reset button – used to restart the system without disconnecting the Power supply.
  Power indicator – indicates that the system has been powered.
  Power switch – Used to switch on the PC.
  Hard disk/floppy disk/CD indicators – are LEDs that come on when respective disk is being read or written.

## Slide 11: Inside the System Unit
In a typical microcomputer, the system unit contains the power supply, storage devices and the main circuit board with the computer’s main processor and memory.
The Power Supply
This component converts the AC electricity from the outlet to the DC electricity for PC uses. A fan keeps the power supply and other components in the system unit from overheating.

## Slide 12
The Main board/Motherboard.
This is the main circuit board that houses the integrated circuits in the system unit. It contains the microprocessor, the RAM, expansion cards and is connected to peripheral devices that collect input and produce output.
Memory
Memory is electronic circuitry that holds the data and program instruction. It is sometimes called primary storage. There are four major types of memory, namely random access memory (RAM), virtual memory, CMOS memory and read-only memory (ROM).

## Slide 13: Memory
Memory
RAM
SRAM
DRAM
ROM
PROM
EPROM

## Slide 14: Memory
Random Access Memory (RAM)
This is an area in the computer system unit that temporarily holds data before and after it is processed. For example, when you enter a document, the characters you type usually are not processed right away. They are held in RAM until you tell the software to carry out process such as printing.
In RAM, the microscopic electronic parts called capacitor hold the electronic signals for the binary codes that represent the data. RAM is volatile i.e. if the computer is turned off or the power goes out, all the data stored in RAM instantly and permanently disappears.

## Slide 15: Functions of the RAM
The contents of RAM are necessary for the computer to process any data. The CPU receives instructions from RAM, uses the data in RAM for processing and keeps the results of processing temporarily in RAM until they are needed again or stored on disk.
RAM stores user data, operating system instructions and program instructions temporarily. Every time you turn on your computer, it copies a set of operating system instructions from disk into RAM. These instructions, which help control basic computer functions, remain in RAM until you turn the computer off.
RAM also holds program instructions. When you use a word processing program, the computer copies the instructions that turn your computer into a word processor from disk into RAM.

## Slide 16: RAM capacity
The storage capacity of RAM is measured in megabytes (MB) or Gigabytes (GB).
Most recent micro-computers have between 128 MB – 2 GB of RAM.
The amount of RAM your computer needs depends on the software you use.

## Slide 17: Read Only Memory (ROM)
This is a set of chips containing instructions that help a computer prepare for processing tasks. These instructions also called firmware are permanent, and the only way to change them is to remove the ROM chips from the main board and replace them with another set.
When you turn on your computer, the CPU receives electrical power and is ready to begin executing instructions. But because the computer was turned on, RAM is empty with no instructions for CPU to process. This is when ROM finds its use.
When you turn on your computer, the CPU performs a series of steps by following instructions stored in ROM. This series of steps is called the boot process.

## Slide 18: Types of ROM
Programmable read-only memory (PROM) - acts the same as ROM when it is part of the computer. I.e. it can only be read but its contents cannot be altered. However the data or programs are not stored in the memory when they are manufactured. Instead it can be loaded with special programs during installation.
Erasable Prom (EPROM) - their data can be erased using special ultraviolet light device that destroys the bit settings within the memory.

## Slide 19: Virtual Memory
The computer sometimes uses space on the computers hard disk as an extension of RAM. A computer’s ability to use disk storage to simulate RAM is called virtual memory.
Virtual memory allows computers without enough real memory to run large programs, manipulate large data files and run more than one program at a time. One disadvantage of a virtual memory is reduced performance.

## Slide 20: CMOS Memory
Complementary Metal oxide semi conductor memory.
This is a type of memory which is more permanent than RAM but less permanent than ROM which is used to store boot data such as the number of hard disk tracks and sections. CMOS require very little power to retain its contents and as such can be powered by battery.
To change CMOS data, you usually run a CMOS configuration, or set up program.

## Slide 21: Memory
SRAM: Static RAM
Random Access Memory
DRAM: Dynamic RAM
EPROM: Erasable Programmable ROM
PROM: Programmable ROM
Read Only Memory
1 MB
2 MB
4 MB
8 MB
16 MB
32 MB
64 MB
128 MB
256 MB
512 MB
1024 MB
Extra Points: What mathematical equation
describes the pattern?
Memory Size in MB

## Slide 22: The Central Processing Unit (CPU)
This is the circuitry in a computer that executes instructions to process data.
CPU is the heart of the computer system.
It retrieves instructions and data from RAM, processes them and places the result back into RAM so they can be displayed or stored.

## Slide 23: CPU Architecture
The CPU consists of one or more integrated circuits. In microcomputer the CPU is a single integrated circuit called a micro-processor.
The CPU has two main parts; the arithmetic logic unit (ALU) and the control unit (CU).
The ALU (Arithmetic Logic Unit) performs arithmetic operations such as addition, subtraction, division and multiplication.
It also performs logical operations such as comparing two numbers. It uses registers to hold the data that is being processed.
In ALU, the results of an arithmetic or logical operation is held temporarily in the accumulator.
The CU (Control Unit) - directs and coordinates processing and places it in a special instruction register.
The CU then interprets the instruction to find out what needs to be done. According to its interpretation, the control unit sends signals to the data bus to fetch data from RAM, and to the ALU to perform a process.

## Slide 24: Factors that influence the CPU Performance
Clock rate
Word size
Cache
Instruction set size.

## Slide 25
Clock rate
A computer contains a system clock that emits pulses to establish the timing for all system operations. The “system clock” is not the same as “real-time clock” that keeps track of the time of day.
The system clock sets the speed for data transport and instruction execution. The clock rate set by the system clock determines the speed at which the computer can execute an instruction. The time to complete an instruction circle is measured in megahertz (MHz).
Word Size
This refers to the number of bits the CPU can manipulate at a time. e.g. CPU with 8 - bit word size is referred to as an 8 -bit processor. Today’s faster computers use 32 bit or 64 - bit microprocessors.
Cache
This is a special high-speed memory that give the CPU more rapid access to data. As you begin a task, the computer anticipates what data the CPU is likely to need and loads or caches this data into the cache area. The CPU then takes the data from cache instead of fetching it from RAM, which takes longer. Therefore more cache means faster processing.
Instruction Set Complexity
A computer with a complex instruction set is known as a complex instruction set computer (CISC). A computer whose CPU has a reduced instruction set called a reduced instruction set computer (RISC) has a limited set of instruction that it performs very quickly. Therefore RISC machine is faster than CISC machine for most processing tasks.

## Slide 26: Output Devices
Output is the data that has been processed into useful form/information that can be used by a person or a machine.
Most outputs are in form of reports or graphics. The most used output devices are:-
Printers
Printers can be classified by how they transfer characters from the printer to the paper.
  Impact Printers
Transfer images into paper by some type of printing mechanism striking paper, ribbon, and character together.
  Non-Impact Printers
Printing occurs without having a mechanism striking against a sheet of paper.
Speed

## Slide 27: Printers
Output Devices
Hard Copy Output
Resolution is given in “dsi”. Dots per Inch.
Two Categories:
  Laser (B&W, Color) uses Toner.
  Inkjet (Color) uses ink cartridges.

## Slide 28: Classifying Printers By their Speed
Another way of classifying printers is by speed:-
Low speed printers- print one character at a time.
Medium and high-speed printers - called line printers, can print multiple characters on a line at the same time.
Very high-speed printers - can print excess of 3,000 lines per minute, often called page printers.

## Slide 29: Types of Printers
Dot Matrix Printers
Create letters and graphics by striking an inked ribbon with a column of small wires called pins. By activating some wires in the column, but not activating others, the printer creates patterns for letters and numbers.
Advantages
Low operating costs
Low price
Can print multi-part forms – Make carbon copies
Durable
Limitations
Noisy
Low to medium quality output
Slow

## Slide 30
Ink-jet Printers
Produce characters and graphics by spraying ink onto paper. The print-head is a matrix of fire spray nozzles, patterns are created by activating selected nozzles.
Advantages
Moderate price
Inexpensive to operate
High quality color printouts/high quality output.
Quiet
Durable
Disadvantages
Slow
Cannot print multi-part forms – cannot make carbon copies
Poor quality colour compared to laser printers

## Slide 31
Laser Printers
Use the same technology as the duplicating machines.
Advantages
Quiet
High quality output
Fast
High quality color
Durable
Limitations
Expensive color
Cannot print multi-part forms
More expensive to operate

## Slide 32: Others
Daisy wheel printers
Thermal printers
Chain printers
Band printers

## Slide 33: The Monitor (The Screen)
Also called cathode ray tube (CRT) or video display terminal (VDT).
It lets you see the information you are exchanging with the computer.
They can be either monochrome or color. Monochrome display only two colors, either black and white or green and black.
The size is measured diagonally (like TV) in inches e.g. 14”.
Inside the monitor is a video display adapter, which is an expansion card that translates the signal, processed by the CPU into a format that the monitor can display.

## Slide 34: Monitors
Output device,
Soft-Copy Output
Resolution is given by the amount of “Pixels”
Two categories:
  CRT (Cathode Ray Tubes)
  LCD (Liquid Crystal Display)

## Slide 35: Other Outputting Devices
Plotters
Used to produce high-quality line drawing, such as building plans, charts or circuit diagrams. The two types are (a) pen plotters - create image on a sheet of paper by moving the paper under the tip of pen (b) electrostatic plotters.
Computer Output Microfilm
COM is an output technique that records output from a computer as microscopic images on roll or sheet film.
Voice Output
Consist of spoken words that are conveyed to the user from the computer. The data that produces voice output is usually created in one of two ways:-
A person can talk into a device that will encode the words in digital pattern. The digital data is then stored on a disk. It can later be translated back from digital data into voice.
Voice Synthesizer:- can transform words stored in main memory into speech.

## Slide 36: Auxiliary/Secondary Storage
Stores programs and data when they are not being processed. They are non-volatile ie. data and programs are retained when the power is turned off.
Hard Disk:
This is where most of the computer data is stored especially the programs and personal files. It consists of one or more rigid metal platters coated with a metal oxide material that allows data to be magnetically recorded on the surface of the platter.
Floppy Disks/Diskettes/Floppies/Disks
Consists of a circular piece of a thin Mylar plastic (actual disk) which is coated with oxide material. The circular piece is enclosed in a flexible square plastic jacket.
This type of storage is convenient, reliable and relatively low in cost. The storage capacity ranges between 360 K to 2.88 MB. They come in several sizes: Most common being 3½ inch.
Magnetic Disk
This is used for medium and large computers. They are similar to the devices used in PC’s but have larger capacities.